## Slide 1
ND-500 Instruction Operand Map
Data Types, Addressing Modes, and Operand Support
241 instructions | 7 data type prefixes | 6 addressing modes

## Slide 2
Data Type Prefixes
BI
Bit — Single bit operations
BY
Byte — 8-bit integer
H
Halfword — 16-bit integer
W
Word — 32-bit integer
F
Float — 32-bit IEEE 754
D
Double — 64-bit IEEE 754
R_N
Real N — Extended precision

## Slide 3
Addressing Modes
CON
CONSTANT — Immediate value in instruction
LOC
LOCAL — Stack-relative via B register
REC
RECORD — Record-relative via R register
REG
REGISTER — CPU register direct
ABS
ABSOLUTE — Direct memory address
PRE
PRE_INDEXED — Base + index addressing

## Slide 4
Instructions by Category
MOVE: 56 instructions
ARITHMETIC: 37 instructions
SYSTEM: 35 instructions
FLOAT_MATH: 25 instructions
BRANCH: 20 instructions
CALL: 18 instructions
STRING: 18 instructions
CONTROL: 9 instructions
BITFIELD: 7 instructions
LOGICAL: 5 instructions
COMPARE: 5 instructions
SHIFT: 5 instructions
IO: 1 instructions

## Slide 5
Operand Support (1/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
*
Multiply
ARITHMETIC
1
BY, D, F, H, R_N,
ABS, CON, LOC, PRE, REC, REG
-
+
Add
ARITHMETIC
1
BY, D, F, H, R_N,
ABS, CON, LOC, PRE, REC, REG
-
-
Subtract
ARITHMETIC
1
BY, D, F, H, R_N,
ABS, CON, LOC, PRE, REC, REG
-
/
Divide
ARITHMETIC
1
BY, D, F, H, R_N,
ABS, CON, LOC, PRE, REC, REG
-
:=
AssignTo
MOVE
1
BI, BY, D, F, H, R
ABS, CON, LOC, PRE, REC, REG
-
=:
AssignFrom
MOVE
1
BI, BY, D, F, H, R
ABS, LOC, PRE, REC, REG
-
a1:=
A1Set
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
a1=:
A1Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
a2:=
A2Set
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
a2=:
A2Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
a3:=
A3Set
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
a3=:
A3Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
a4:=
A4Set
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
a4=:
A4Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
abs
Abs
ARITHMETIC
0
BY, D, F, H, R_N,
-
-
acos
Acos
FLOAT_MATH
1
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
-
add2
Add2
ARITHMETIC
2
BY, D, F, H, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
add3
Add3
ARITHMETIC
3
BY, D, F, H, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG

## Slide 6
Operand Support (2/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
addc
Addc
ARITHMETIC
1
R_N, W
ABS, CON, LOC, PRE, REC, REG
-
alog
Alog
FLOAT_MATH
1
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
-
alog10
Alog10
FLOAT_MATH
1
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
-
alog2
Alog2
FLOAT_MATH
1
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
-
and
And
LOGICAL
1
BI, BY, H, R_N, W
ABS, CON, LOC, PRE, REC, REG
-
asin
Asin
FLOAT_MATH
1
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
-
atan
Atan
FLOAT_MATH
1
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
-
atan2
Atan2
FLOAT_MATH
2
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
axi
Axi
ARITHMETIC
2
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
b:=
AssignBaseRegTo
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
b=:
AssignToBaseReg
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
biconv
Biconv
FLOAT_MATH
2
BY, D, F, H, W
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG
bladdr
Bladdr
SYSTEM
1
BI, BY, D, F, H, W
ABS, LOC, PRE, REC
-
bmove
Bmove
MOVE
3
BY, D, F, H, W
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC
bp
Bp
CONTROL
0
-
-
-
byconr
Byconr
FLOAT_MATH
2
D, F
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG
byconv
Byconv
FLOAT_MATH
2
BI, D, F, H, W
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG
cad:=
CadSet
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-

## Slide 7
Operand Support (3/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
cad=:
CadGet
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
call
Call
CALL
2
-
-
CON
callg
Callg
CALL
2
-
ABS, CON, LOC, PRE, REC, REG
CON
ced=:
CedGet
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
chain
Chain
CALL
3
R_N, W
ABS, LOC, PRE, REC
ABS, CON, LOC, PRE, REC, REG
cind
Cind
SYSTEM
3
BY, H, R_N, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
clebi
Clebi
BITFIELD
2
BY, H, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
clr
Clr
MOVE
0
BI, BY, D, F, H, R
-
-
clrk
Clrk
MOVE
0
-
-
-
clte
Clte
CONTROL
1
-
ABS, CON, LOC, PRE, REC, REG
-
comp
Comp
COMPARE
1
BI, BY, D, F, H, R
ABS, CON, LOC, PRE, REC, REG
-
comp2
Comp2
COMPARE
2
BI, BY, D, F, H, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
cos
Cos
FLOAT_MATH
1
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
-
cpgu
Cpgu
SYSTEM
0
-
-
-
cte1=:
Cte1Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
cte2=:
Cte2Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
cwip
Cwip
SYSTEM
0
-
-
-
dcc
Dcc
SYSTEM
0
-
-
-

## Slide 8
Operand Support (4/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
dconv
Dconv
FLOAT_MATH
2
BI, BY, F, H, W
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG
dctsb
Dctsb
SYSTEM
0
-
-
-
ddirt
Ddirt
SYSTEM
0
-
-
-
decr
Decr
ARITHMETIC
1
BY, D, F, H, W
ABS, LOC, PRE, REC, REG
-
div2
Div2
ARITHMETIC
2
BY, D, F, H, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
div3
Div3
ARITHMETIC
3
BY, D, F, H, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
div4
Div4
ARITHMETIC
3
BY, H, R_N, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
dmof
Dmof
SYSTEM
0
-
-
-
dmon
Dmon
SYSTEM
0
-
-
-
e1:=
E1Set
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
e1=:
E1Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
e2:=
E2Set
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
e2=:
E2Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
e3:=
E3Set
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
e3=:
E3Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
e4:=
E4Set
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
e4=:
E4Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
entb
Entb
CALL
1
-
ABS, CON, LOC, PRE, REC, REG
-

## Slide 9
Operand Support (5/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
entd
Entd
CALL
0
-
-
-
entf
Entf
CALL
1
-
-
-
entfn
Entfn
CALL
2
-
-
ABS, CON, LOC, PRE, REC, REG
entm
Entm
CALL
3
-
-
ABS, CON, LOC, PRE, REC, REG
ents
Ents
CALL
1
-
ABS, CON, LOC, PRE, REC, REG
-
entsn
Entsn
CALL
2
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
entt
Entt
CALL
2
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
exp
Exp
FLOAT_MATH
1
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
-
fconr
Fconr
FLOAT_MATH
2
D, W
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG
fconv
Fconv
FLOAT_MATH
2
BI, BY, D, H, W
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG
freeb
Freeb
SYSTEM
2
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
getb
Getb
BITFIELD
1
R_N, W
ABS, CON, LOC, PRE, REC, REG
-
getbf
Getbf
BITFIELD
3
BY, H, R_N, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
getbi
Getbi
BITFIELD
2
BY, H, R_N, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
go
Go
BRANCH
1
-
-
-
hconr
Hconr
FLOAT_MATH
2
D, F
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG
hconv
Hconv
FLOAT_MATH
2
BI, BY, D, F, W
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG
hl:=
HlSet
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-

## Slide 10
Operand Support (6/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
hl=:
HlGet
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
if-kgo
IfKeyGo
BRANCH
1
-
-
-
if-stgo
IfStackGo
BRANCH
2
-
ABS, CON, LOC, PRE, REC, REG
-
if<<=go
IfUnsignedLessEqua
BRANCH
1
-
-
-
if<<go
IfUnsignedLessGo
BRANCH
1
-
-
-
if<=go
IfLessEqualGo
BRANCH
1
-
-
-
if<go
IfLessThanGo
BRANCH
1
-
-
-
if=go
IfEqualGo
BRANCH
1
-
-
-
if><go
IfNotEqualGo
BRANCH
1
-
-
-
if>=go
IfGreaterEqualGo
BRANCH
1
-
-
-
if>>=go
IfUnsignedGreaterE
BRANCH
1
-
-
-
if>>go
IfUnsignedGreaterG
BRANCH
1
-
-
-
if>go
IfGreaterThanGo
BRANCH
1
-
-
-
ifkgo
Ifkgo
BRANCH
1
-
-
-
ifkret
Ifkret
CALL
0
-
-
-
ifstgo
Ifstgo
BRANCH
2
-
ABS, CON, LOC, PRE, REC, REG
-
incr
Incr
ARITHMETIC
1
BY, D, F, H, W
ABS, LOC, PRE, REC, REG
-
init
Init
CONTROL
3
-
-
ABS, CON, LOC, PRE, REC, REG

## Slide 11
Operand Support (7/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
int
Int
SYSTEM
1
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
-
intr
Intr
SYSTEM
1
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
-
inv
Inv
LOGICAL
0
BI, BY, H, R_N, W
-
-
invc
Invc
LOGICAL
0
R_N, W
-
-
ixi
Ixi
ARITHMETIC
2
BY, H, R_N, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
jumpg
Jumpg
BRANCH
1
-
ABS, CON, LOC, PRE, REC, REG
-
jumps
Jumps
BRANCH
1
-
ABS, CON, LOC, PRE, REC, REG
-
l:=
LSet
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
l=:
LGet
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
laddr
Laddr
SYSTEM
1
BI, BY, D, F, H, R
ABS, LOC, PRE, REC
-
lcntxt
Lcntxt
SYSTEM
3
-
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG
lind
Lind
SYSTEM
3
BY, H, R_N, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
ll:=
LlSet
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
ll=:
LlGet
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
loop
Loop
BRANCH
4
BY, D, F, H, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
loopd
Loopd
BRANCH
3
BY, D, F, H, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
loopi
Loopi
BRANCH
3
BY, D, F, H, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
lregbl
Lregbl
SYSTEM
2
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG

## Slide 12
Operand Support (8/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
move
Move
MOVE
2
BI, BY, D, F, H, W
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG
mte1=:
Mte1Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
mte2=:
Mte2Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
mul2
Mul2
ARITHMETIC
2
BY, D, F, H, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
mul3
Mul3
ARITHMETIC
3
BY, D, F, H, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
mul4
Mul4
ARITHMETIC
3
BY, H, R_N, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
mulad
Mulad
ARITHMETIC
2
BY, D, F, H, R_N,
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
neg
Neg
ARITHMETIC
0
BY, D, F, H, R_N,
-
-
noop
Noop
CONTROL
0
-
-
-
or
Or
LOGICAL
1
BI, BY, H, R_N, W
ABS, CON, LOC, PRE, REC, REG
-
ote1:=
Ote1Set
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
ote1=:
Ote1Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
ote2:=
Ote2Set
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
ote2=:
Ote2Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
p=:
PGet
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
padd
Padd
ARITHMETIC
3
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
paddr
Paddr
ARITHMETIC
3
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
pcc
Pcc
SYSTEM
0
-
-
-

## Slide 13
Operand Support (9/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
pcomp
Pcomp
COMPARE
2
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
pctsb
Pctsb
SYSTEM
0
-
-
-
phyladr
Phyladr
SYSTEM
1
R_N, W
ABS, LOC, PRE, REC
-
pmof
Pmof
SYSTEM
0
-
-
-
pmon
Pmon
SYSTEM
0
-
-
-
pmpy
Pmpy
ARITHMETIC
3
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
pmpyr
Pmpyr
ARITHMETIC
3
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
poly
Poly
FLOAT_MATH
2
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
CON
ppack
Ppack
ARITHMETIC
2
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
ppackr
Ppackr
ARITHMETIC
2
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
ps:=
PsSet
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
ps=:
PsGet
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
pshift
Pshift
SHIFT
2
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
pshiftr
Pshiftr
SHIFT
2
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
psub
Psub
ARITHMETIC
3
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
psubr
Psubr
ARITHMETIC
3
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
psum
Psum
ARITHMETIC
2
BY, D, F, H, R_N,
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
pupack
Pupack
ARITHMETIC
2
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG

## Slide 14
Operand Support (10/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
pupackr
Pupackr
ARITHMETIC
2
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
putbf
Putbf
BITFIELD
3
BY, H, R_N, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
putbi
Putbi
BITFIELD
2
BY, H, R_N, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
pwconv
Pwconv
FLOAT_MATH
1
R_N, W
ABS, CON, LOC, PRE, REC, REG
-
r:=
AssignRecordRegTo
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
r=:
AssignToRecordReg
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
rdus
Rdus
SYSTEM
1
BI, BY, H, R_N, W
ABS, CON, LOC, PRE, REC, REG
-
rem
Rem
ARITHMETIC
3
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
ret
Ret
CALL
0
-
-
-
retb
Retb
CALL
0
-
-
-
retbk
Retbk
CALL
0
-
-
-
retd
Retd
CALL
0
-
-
-
retk
Retk
CALL
0
-
-
-
rett
Rett
CALL
0
-
-
-
riom
Riom
IO
3
H
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
rladdr
Rladdr
SYSTEM
1
BI, BY, D, F, H, W
ABS, LOC, PRE, REC
-
rpgu
Rpgu
SYSTEM
1
BI, H, R_N
ABS, CON, LOC, PRE, REC, REG
-
rphs
Rphs
SYSTEM
1
-
ABS, CON, LOC, PRE, REC, REG
-

## Slide 15
Operand Support (11/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
rwip
Rwip
SYSTEM
1
BI, H, R_N
ABS, CON, LOC, PRE, REC, REG
-
schpar
Schpar
STRING
2
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
scntxt
Scntxt
SYSTEM
2
-
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG
scomp
Scomp
COMPARE
2
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
scopa
Scopa
STRING
3
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
scopt
Scopt
STRING
4
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
scotr
Scotr
STRING
3
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
scpuno
Scpuno
STRING
1
-
ABS, LOC, PRE, REC, REG
-
set1
Set1
CONTROL
1
BI, BY, D, F, H, W
ABS, LOC, PRE, REC, REG
-
setbi
Setbi
BITFIELD
2
BY, H, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
sete
Sete
CONTROL
1
-
ABS, CON, LOC, PRE, REC, REG
-
setk
Setk
CONTROL
0
-
-
-
sfill
Sfill
STRING
1
BI, BY, D, F, H, R
ABS, CON, LOC, PRE, REC, REG
-
sfilln
Sfilln
STRING
2
BI, BY, D, F, H, R
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
sha
Sha
SHIFT
2
BY, H, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
shl
Shl
SHIFT
2
BY, H, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
shr
Shr
SHIFT
2
BY, H, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
sin
Sin
FLOAT_MATH
1
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
-

## Slide 16
Operand Support (12/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
sloca
Sloca
SYSTEM
2
BI, BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
smatch
Smatch
STRING
2
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
smove
Smove
STRING
2
BI, BY, D, F, H, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
smovn
Smovn
STRING
3
BI, BY, D, F, H, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
smvtr
Smvtr
STRING
3
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
smvtu
Smvtu
STRING
3
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
smvun
Smvun
STRING
4
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
smvwh
Smvwh
STRING
4
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
solo
Solo
CONTROL
0
-
-
-
sqrt
Sqrt
FLOAT_MATH
1
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
-
sregbl
Sregbl
SYSTEM
2
-
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
sscan
Sscan
STRING
3
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
sskip
Sskip
STRING
2
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
sspan
Sspan
STRING
3
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
sspar
Sspar
STRING
2
BY
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
st1:=
St1Set
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
st1=:
St1Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
stz
Stz
MOVE
1
BI, BY, D, F, H, W
ABS, LOC, PRE, REC, REG
-

## Slide 17
Operand Support (13/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
sub2
Sub2
ARITHMETIC
2
BY, D, F, H, W
ABS, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
sub3
Sub3
ARITHMETIC
3
BY, D, F, H, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
subc
Subc
ARITHMETIC
1
R_N, W
ABS, CON, LOC, PRE, REC, REG
-
svers
Svers
SYSTEM
1
-
ABS, LOC, PRE, REC, REG
-
swap
Swap
MOVE
2
BI, BY, D, F, H, W
ABS, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG
tan
Tan
FLOAT_MATH
1
D, F, R_N
ABS, CON, LOC, PRE, REC, REG
-
temm1=:
Temm1Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
temm2=:
Temm2Get
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
test
Test
COMPARE
1
BI, BY, D, F, H, W
ABS, CON, LOC, PRE, REC, REG
-
tha:=
ThaSet
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
tha=:
ThaGet
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
tos:=
TosSet
MOVE
1
-
ABS, CON, LOC, PRE, REC, REG
-
tos=:
TosGet
MOVE
1
-
ABS, LOC, PRE, REC, REG
-
tset
Tset
CONTROL
1
BY
ABS, LOC, PRE, REC, REG
-
tutti
Tutti
SYSTEM
0
-
-
-
udiv
Udiv
ARITHMETIC
3
R_N, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
umul
Umul
ARITHMETIC
3
R_N, W
ABS, CON, LOC, PRE, REC, REG
ABS, CON, LOC, PRE, REC, REG
wconr
Wconr
FLOAT_MATH
2
D, F
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG

## Slide 18
Operand Support (14/14)
Instr
Name
Cat
#
Prefixes
Op1 Modes
Op2 Modes
wconv
Wconv
FLOAT_MATH
2
BI, BY, D, F, H
ABS, CON, LOC, PRE, REC, REG
ABS, LOC, PRE, REC, REG
wdus
Wdus
SYSTEM
1
BY, H, R_N, W
ABS, CON, LOC, PRE, REC, REG
-
wpconv
Wpconv
FLOAT_MATH
1
R_N, W
ABS, CON, LOC, PRE, REC, REG
-
wphs
Wphs
SYSTEM
1
-
ABS, CON, LOC, PRE, REC, REG
-
xor
Xor
LOGICAL
1
BI, BY, H, R_N, W
ABS, CON, LOC, PRE, REC, REG
-
zpgu
Zpgu
SYSTEM
1
BI
ABS, CON, LOC, PRE, REC, REG
-
zwip
Zwip
SYSTEM
1
BI
ABS, CON, LOC, PRE, REC, REG
-